An Optical 6-axis Force Sensor for Brain Function Analysis using fMRl

Norihisa TAKAHASHI

Mitsunori TADA

Jun UEDA

Yoshio MATSUMOTO

Tsukasa OGASAWARA

2003 IEEE 253-258

Problems with previous MR-compatible force sensors have been:

-Not as accurate as conventional sensors

-Robustness not enough against the contact force to the optical fibers

-Not suitable for projection to 6-axis sensors

Proposed Sensor:

-Based on Hirose’s optical sensor with 4-segmented photo-diode unit and light source.

-Equal to conventional force sensors with strain gauges in accuracy

-Measures forces by change of a quantity of light through the optical fibers.

-Fibers connected with elastic frame.

-Forces applied to frame cause a displacement of fiber with the light source.

-To improve accuracy, light source was stabilized and optical fibers were fixed with the elastic frame. (Described in paper.)

-Output: Fx, Fy, Fz, Mx, My, Mz.

Issues:

-Elastic frame (acrylic resin) causes hysteresis

-Sensor output is nonlinear, and calibration needs to account for it still.

Development of an MR-Compatible Optical Force Sensor

M. Tada

T. Kanade

Proceedings of the 26th Annual International Conference of the IEEE EMBS

San Francisco, CA, USA • September 1-5, 2004

-Also finds the main cause in error of measured force is mechanical oscillation of optical fiber.

-Solves problem by fixing the encoder lens.

-SNR determined with phantom experiments, % loss less than 3%.

Cather Tip Force Sensing FBG Patent

…, 2007

List of fiber optic force sensors on pg7:

Strain calculations with 3 FBG’s, pg 19:

Total strain includes temperature strain. Therefore, elastic strain found from:

Force to strain conversion matrix, explained in pg. 24.