# Body/appendage development

creation of soft chambers, selectively reinforced with high-strength tensile fibers for controlled combinations of extension and contraction when actuated or pushed into confining spaces

For main proposal body: Whereas many soft-bodied animals use hydrostats (arrangements of orthogonal muscles such that, for example, radial contraction results in axial expansion) peroxide requires the opposite approach: volumetric expansion produces axial extension accompanied by radial contraction or stasis.

## modular tentacle v1

## two degrees of freedom: forward and left/right. Able to steer toward and traverse a small aperture. Basic sensing. (recheck Phase I objectives)

## tristar v2

## Created essentially from 4 tentacle modules with shape changing DOF. able to transform between linear (worm) and branched (sea star, octopus) configurations. Able to grasp and move objects and climb (e.g. climb a pole or a rock). Able to self-anchor for pushing into cracks.

## polypod v3

## Created from central core and multiple tentacles. Able to locomote comparatively rapidly, to climb, to grasp and perform simple manipulations on objects.

# Electronics

## battery and power distribution

## signal and processing

## control

## flexible electronics integration and testing

# Communication

## internal communication

## external communication

# Power source and conversion

## energy storage and distribution

robot is self-consuming as the peroxide is used both as power source and as incompressible fluid for pseudo-hydrostat

## analysis of volume required as function of mission duration (see energy analysis below)

## valving and catalysis

## valving of microliters of fluid at low pressure. catalysis inside the actuator. Possibility for passive, timed exhaust via leakage

## thermal management

## thermal capacity and heat transfer to ensure that maximum permissible temperatures of skin, valves, sensors are never exceeded. Thermal analysis also related to thermodynamic cycle efficiency (see energy analysis below)

# Integrated actuator development

## structural analysis

## expansion and PV calculations for locomotion, morphing. Analysis of pressures and material strains. Limits on parametric dimensional variations. Fiber strength and density.

## exit valving

## active versus passive exit valving, phase timing. Exit valve development.

## energy analysis

thermodynamic cycle and overall actuation efficiency. Minutes of operation per microliter of peroxide.

## Analysis of power capacity, efficiency, volume required per minute of operation as a function of actuation type and speed.

# Sensing

## mechanical sensing

## development of whisker and antennae sensors – light, robust, simple and highly flexible.

## optical sensing

## optical proximity sensors and possible simple imaging and pattern recognition for aperture detection

## sensor integration, power and signal distribution

## Sensors are anchored into flexible skin and power/signal distribution system.

# Low level control

## gait determination

## phasing

## mobility analysis, efficiency

# Behaviors

# open terrain locomotion

# various locomotion types depending on platform. Simplest = annelid (worm like) wave. More advanced methods include walking with body raised by tentacle legs.

# aperture detection, location

# integration of information from mechanical and optical sensors, basic pattern recognition for aperture detection and alignment

# aperture traversal

# locomotion specialized for crawling through aperture. (Mainly passively constrained and utilizing directional skin to ensure forward movement.)

# reconstitution

# recovery of open-terrain shape upon exiting aperture

# morphing

# changing configuration (e.g. from linear to branched) utilizing specialized low-power shape-changing actuators that operate between two latched, stable states.

# payload tasks

# depositing payload, retrieving a payload. More advanced  tasks possible during Phase II.

# grasping, climbing

# in branched configuration – wrapping around compact (e.g. cylindrical objects) to climb or move them.

# other mission objectives

# Depending on guidance for Phase II – could include specific surveillance, manipulation, chemical testing or other tasks.

# Systems integration and testing

# v1 tentacle testing (Phase I)

initial open-terrain testing for speed, endurance

initial test through aperture (manually positioned)

# test through aperture without manual pre-positioning

# v2 starbot

demonstrate shape change

# demonstrate ability to execute coordinated grasp & push operations in addition to all capabilities of v1 tentacle

# v3 polypod

demonstrate shape change (expanded versus flattened)

demonstrate coordinated walking locomotion

# demonstrate ability to execute coordinated grasp & push operations in addition to all capabilities of v1 tentacle