Selectively Compliant, Reconfigurable Chembots
for Traversing Tight Spaces

A white paper submitted in response to DARPA BAA BAA07-21, CHEMICAL ROBOTS
DARPA Contact: Dr. Mitchell R. Zakin, DARPA/DS0; baa07-21@darpa.mil

Date: 25 June, 2007

Estimated cost:

Phase I (18 months): $1,915,467

Proposing Team Technical Point of Contact:

Mark R. Cutkosky
Professor
Department of Mechanical Engineering
Terman 523
Leland Stanford Jr. University
Stanford, CA 94305-4021
(650) 725-1588, fax: (650) 723-3521
cutkosky@stanford.edu

# Executive Summary

This proposal offers a unique and highly feasible approach to the development of a soft mesoscale robot, capable of squeezing through an opening that is significantly smaller than its characteristic size. The approach draws inspiration from invertebrates that use hydraulic pressure for locomotion and whose tissues undergo large mechanical strains to pass through narrow openings, afterward regaining their original shape and dimensions.

Our robot will use hydrogen peroxide as a chemical energy source that is inherently deformable and has a high energy density. Small amounts of liquid peroxide will be controlled using micro-dispensing valves and expanded, using a catalyst, inside the elastic actuation chambers of the robot.

Whereas highly deformable invertebrates typically change shape by contracting radial muscles and expanding axially, our robot uses active volumetric expansion followed by passive elastic contraction. The elastic units are fabricated using a variation of the Shape Deposition Manufacturing process that we have used in previous bio-inspired robots and will be composed of silicone and urethane materials capable of several hundred percent strain. To achieve selective stiffness on demand, the elastic skin is reinforced with, and expands against, embedded fibers (e.g. Kevlar) and wires of super-elastic Nitinol alloy. Nitinol can also be employed for miniature, low-power actuators (e.g. for latching two modules together).

Our research plan involves a graded series of accomplishments culminating in an autonomous, highly deformable chembot that can meet the Phase I objectives in Table I. We will begin with the design, analysis and fabrication of basic worm-like “tentacle” units (Figure 1) that can locomote with a peristaltic wave gait and steer left/right and up/down to navigate toward holes. The main actuation will be open loop, governed by a central pattern generator that triggers the valves with a specified phase. The tentacle units will be covered with directional skin and spines so that they can push forward and into narrow openings. In parallel we will conduct tests of external communication using RF and optical methods and navigation using a miniature camera and simple optical and mechanical sensors to ensure that the unit can approach an aperture from the appropriate angle, deflate the distal segment, push into the aperture, proceed forward by peristaltic waves and reinflate upon exiting.

Ultimately, we envision multiple tentacles that can assemble into more complex configurations (e.g. branched or multi-legged) with additional capabilities such as legged locomotion and climbing or grasping objects.

The proposed approach leverages a core team with prior achievements in liquid chemical power and actuation [Goldfarb03] and compliant bio-inspired running and climbing robots [Cham02]. During Phase I we additionally benefit from the consultation and electronics and control development of S. Potter of the Foster Miller Inc. Robotics group. In Phase II, Foster Miller Inc. can provide a path toward pre-commercial prototypes for testing in applications scenarios. Finally, we take advantage of Cutkosky’s interaction with the laboratory of Prof. Paolo Dario in Pisa, Italy. Dario’s laboratory is a leading European center in bio-robotics and has constructed worm, lamprey and polychaete inspired robots that are widely cited in the literature. Although these robots are only moderately deformable, they can be used for testing particular sensing and guidance strategies while developing, concurrently, the primary actuation and body mechanisms for our soft Chembot.

Response to comments on the previously submitted whitepaper

1. Phase I metrics for open area locomotion and traversal through 1cm x 1cm openings are summarized in Table I. Details of the supporting analysis are provided in the following section of this proposal.

2. A 70% H2O2 is an explosive and can have limited shelf life. At low ambient temperatures (approximately -30 ºF), water condensation might cause problems with your locomotion system. Do you have other potential power sources? At what temperature will the peroxide freeze?

Response: A 70% mixture of H2O2 is not an explosion hazard, is not flammable and is insensitive to shock [MSDS Ref. No. 7722-84-1-5 (FMC)]. It reacts in contact with organics but has a shelf life measured in years when stored in Class 1 materials, which include metals such as 316 stainless steel and elastomers such as Dow Corning Silastic. Further details are discussed in Section 3.2.

Regarding use in cold environments, neither condensation nor freezing should be a problem. The freezing point for 70% peroxide is -40C. The freezing point is a function of concentration, with the lowest freezing point of -55C corresponding to 60%. Thus, if one wishes to use a soft robot at temperatures lower than -40 C, one can use a slightly more dilute concentration of peroxide in exchange for somewhat less energy density. Peroxide has been used extensively in space applications for satellite thrusters and in naval applications for torpedoes, both of which require low temperature operation.

In addition to the peroxide we require an electrical power source for powering valves, sensors and electronics. For this purpose we plan to use flexible lithium polymer batteries. We have chosen valves that latch in the on or off state to minimize power consumption.

In summary, we use H2O2 as a completely deformable energy source with high energy density and excellent controllability and without the complications of combustible liquid fuels.  We have worked with peroxide for nearly a decade, and have a high degree of competence and working knowledge of its properties and capabilities.  We regard the use of peroxide as a power source as a low risk component of the proposed work. Indeed, a highly deformable Chembot is a nearly ideal application for peroxide, and a broader opportunity of our partnership with Foster Miller Inc. is to introduce peroxide as a practical fuel for specialized applications such as soft mobile robots.

Contents:

1.	Executive Summary	2

2.	Vision	5

3.	Technical Approach	6

3.1.	Bio-Inspiration	6

3.2.	Chemical energy conversion	7

3.3.	Chembot Body design and locomotion	8

3.3.1.	Chembot concept 1: Annelid locomotion	9

3.3.2.	Chembot concept 2: selectively morphing with asymmetric units	10

3.4.	Materials and device fabrication	11

3.4.1.	Sensing and Control	12

3.4.2.	Operational challenges and steps taken to address them	13

4.	Phase I Proposed Plan of Work and Milestones	15

5.	Relevant Prior Work	18

6.	Facilities and Equipment	19

6.1.	UNIVERSITY OF CALIFORNIA, BERKELEY, Department of Integrative Biology, PolyPEDAL Lab	19

6.2.	STANFORD UNIVERSITY, Department of Mechanical Engineering:  Center for Design Research and Rapid Prototyping Lab	20

6.3.	Vanderbilt University	20

6.4.	Foster Miller	20

7.	Management Plan	20

7.1.	Personnel	21

8.	Current and Pending Support	23

9.	References	24

# Vision

In nature, the ability to reconfigure body shape can mean the difference between eating and starving – or between escaping and being eaten. Octopi, onycophorans (e.g. peripatus) and echinoderms (e.g. sea stars) are diverse examples of creatures that force themselves through holes or gaps whose least dimension is small compared to the normal dimensions of their bodies. They also can exert powerful forces, as when sea stars open shells, and negotiate rough terrain with ease. Inspired by these examples, we envision selectively compliant, chemically powered robots that undergo dramatic changes in dimensions and shape, according to changing task requirements. In open terrain, they proceed comparatively rapidly, crawling along on elastic segments or appendages, aided by skin and spines with directional adhesion and friction. In the flattened or extruded state they pass through slits or holes to gain access to locations otherwise denied, or to evade detection. As they exit an aperture, they recover their initial configuration, or even assemble themselves into a new one with different functional characteristics. With this combination of capabilities they can undertake missions that no current legged, wheeled or serpentine robots can accomplish.

The fundamental unit of each robot is a worm-like tentacle, consisting of highly elastic chambers, selectively reinforced with embedded fibers. The units are powered by a 70% hydrogen peroxide (H2O2) solution, an inherently deformable power source with energy density. The peroxide is catalyzed directly in the actuating chambers for simplicity, efficiency, and ease of control. Operating at low pressures and with low flow rates, the robots are quiet and can passively conform to the shapes of obstacles around them.

To further simplify control and to minimize the amount components such as valves and electronics, the robots use tuned passive compliance and damping in combination with an open-loop actuation pattern, following the principles successful used on previous bio-inspired running robots such as RHex [Saranli01] and Sprawl [Cham02].

Upon encountering a barrier, the robots search, using antennae, and possibly additional non-contact visual or proximity sensors, for cracks or holes into which they can force themselves. To enter, the robot establishes a firm grip using directional adhesive patches and spines, adapted from bio-inspired climbing robots [Kim07, Asbeck06], and deflates its distal end. A sequence of open-loop motions then forces the unit into the aperture. Locomotion proceeds slowly within the aperture, aided by directional friction/adhesion skin and spines. Upon exiting, the tentacle unit re-expands, segment by segment, to recover its original shape.

Multiple segments can be joined end-to-end, or fastened at their midpoints to create more complex configurations with additional capabilities
(Figure 3).

# Technical Approach

To traverse a small opening, a robot can decompose itself into constituent parts or it can change shape. We adopt the latter approach and, taking a cue from primitive animals such as annelids and onycophorans (e.g. Peripatus), we emphasize a primarily passive approach to shape change, in which the geometry of the aperture governs the deformation of the body. This approach simplifies control but it requires (1) a highly deformable elastic body and appendages that can flatten or retract, (2) the ability to sense when apertures are sufficiently large for entry, (3) adequate traction and motive force to propel the body into the aperture, and (4) the ability to recover normal shape on exiting the aperture. These primary requirements lead to technical challenges and solutions, addressed in the following sections.

## Bio-Inspiration

Drawing on the successes of previous bio-inspired robots, we will ascertain and adapt principles from animals such as annelids and Peripatus (Figure 4). These animals have numerous features that make them particularly well suited to robotic emulation. For example, Peripatus are soft-bodied, but have limbs, tipped with chitinous claws that they can move and extend with variations in blood pressure. With their soft bodies, they excel at hiding “… in incredibly tight crevices” [Cuevas07] which they locate with anterior antennae. In addition, their relatively primitive neural systems and numerous external sensors including antennae, bristles, and simple visual sensors make them an ideal source of inspiration.

For the current proposal, there are several key questions that we aim to address with experiments on selected invertebrates, similar to experiments conducted by [Quillin00] at U.C. Berkeley on annelids:

How do the animals anchor themselves to get sufficient force to propel into opening?

How are directional spines used to advantage in this context?

What are the maximum changes in body dimensions and are they apparently limited by maximum tissue strain or by maximum muscle contraction?

How is locomotion modified within a confined space (e.g. a tube)?

## Chemical energy conversion

The main power source for the robot will be a hydrogen peroxide monopropellant, which has been demonstrated in previous work [Shields06, Fite06, Goldfarb03] as a compact energy source for robot actuation. The liquid peroxide will also be a working hydraulic fluid for extending and powering limbs; hence, the robot will be self-consuming. Unlike electric motors or engines for combusting liquid fuels, the monopropellant does not require rigid structures for energy conversion and power transmission. Consequently, it is particularly well suited for integration with compliant, under-actuated structures. With miniature valves and a catalyst integrated into the actuators, the entire energy storage, conversion and transmission system is capable of being reconfigured from one shape to another while remaining operational.

A 70% concentration of hydrogen peroxide (H2O2) is a clear, stable liquid at temperatures between -40 and +125 C. On contact with a catalyst it decomposes exothermically to water vapor and oxygen. Based on the conservative assumption of isothermal expansion, 70% peroxide will produce 210 kJ/kg of propellant (or 275 kJ/L) of mechanical energy.  70% peroxide robot actuation systems have been shown to provide an energetic figure of merit [Goldfarb03] an order of magnitude greater than (secondary) battery and electric motor actuation systems [Shields06, Fite06]. Under adiabatic conditions, the maximum temperature of the vapor is 232 C (450 F), which is within the range of operating temperatures for several plastics and elastomers, such as Teflon and PEEK (polyetheretherketone), and silicone and Viton elastomers.

Goldfarb has considerable experience with the design and control of peroxide-powered conventional (hard component) robots and has also tested peroxide-powered Viton-based elastomeric actuators to over 100,000 cycles of loaded actuation.

Though the elastomeric actuators can take several forms, perhaps the simplest is the pleated pneumatic artificial muscle (PPAM) shown in Figure 5. In this form, an elastomeric tube contains longitudinal embedded fibers so that, when pressurized, the fibers remain at constant length and the tube contracts, much like a biological muscle, producing rectilinear contractions of 40% [Daerden02].

In other configurations, the actuation can be multi-directional, as determined by the shape of the actuator and the direction and orientation of the inextensible fibers. For example, an asymmetric actuator can be made to bend and an actuator with spiral fibers will twist and contract [Shinichi01].

In the schematic power and actuation system in Figure 6, the peroxide is stored in and pressurized by the elastomer bladder, fabricated from a Silastic elastomer or Viton (depending on desired durometer), both of which are fully compatible with peroxide. Actuation is initiated by pulsing open the micro-dispensing valve, thus passing a shot of liquid peroxide into the muscle actuator. The actuator is filled with a granular catalyst (iridium-coated alumina granules, 18-20 mesh, with sub-millimeter diameters). A small “stent” of stainless steel wire holds the granules in place and prevents total collapse on deflation.

Muscle relaxation is forced by the elasticity of the skeletal system, and in its simplest form results from a bleed orifice at the far end of the actuator (Figure 7). In this configuration, muscle contraction decays at a predetermined rate. Thus, contraction lasts for a specified time and the module deflates as exhaust gas is dissipated through the permeable ring. The only rigid component is the micro-dispensing valve, which can have dimensions of 3.0 mm (0.11 in) in diameter and 9.6 mm (0.38 in) in length.

H2O2 Risks and Mitigation Factors

Despite its attractive energy density, H2O2 has not seen wide use in robots, partly because it requires care in handling and partly because it is more complicated to control than electric motors. However, it has been used for many years in space applications and in specialized applications such as torpedoes. A 70% mixture of H2O2 is not an explosion hazard, is not flammable, and has been shown to be insensitive to shock. From MSDS Ref. No. 7722-84-1-5 (FMC), the complete entry under the category "Fire/Explosion Hazard" is as follows: "Product is non-combustible. On decomposition releases oxygen which may intensify fire. An explosion hazard when mixed with organics at high concentrations." We do not plan to mix H2O2 with organic compounds. Peroxide has a shelf life measured in years when stored in Class 1 materials, some of which include 316 stainless steel, 6061 aluminum, Teflon, Polyetheretherketone (PEEK), and Dow Corning Silastic elastomers [Gostowski03]. The freezing point for 70% peroxide is -40C; however a 60% solution has a minimum freezing point of -55C. Also, the exothermic catalytic decomposition of the peroxide will aid in keeping the internal temperatures above ambient.

## Chembot Body design and locomotion

While H2O2 offers advantages in terms of high energy density, controllability and inherent deformability, there are also particular challenges in terms of harnessing it to a soft robot that can propel itself over terrain, squeeze through narrow apertures and reconfigure itself. When we examine the anatomy and physiology of invertebrates that excel at these behaviors, we find that in most cases they rely on muscular hydrostats in which annular rings of muscles contract against a constant fluid volume to produce axial extension; conversely, axial contraction produces radial expansion. Keeping the two sets of muscles in opposition allows for local stiffening, which provides the strength required for an animal to raise itself above the ground (e.g. to enter a hole that is not at ground level, or to climb over obstacles) and to force itself into narrow openings.  In the present case, we harness the liquid/gas phase transition of catalyzed H2O2 to produce a volumetric expansion accompanied by a rise in pressure. This mechanical energy must be harnessed to produce a periodic combination of axial extension and radial contraction. We present two variations on “annelid” (worm-like) and “tentacle” designs for achieving the desired effect. The former is more conservative and easier to manufacture; the latter has the potential for considerably greater locomotion per gram of H2O2 consumed but presents somewhat more risk for the manufacturing approach described in the next section.

### Chembot concept 1: Annelid locomotion

The annelid concept shown in Figure 8 propels itself with a peristaltic wave of contractions. The forward end could contain a small camera. Electronics to power valves are located in the tail. Due to the slightly angled units and the fact that each unit is equipped with a directional skin, the entire annelid can be made to veer left or right by selectively actuating modules.

Expected performance

Locomotion occurs through the repitition of cycles of expansion and contraction. In the following calculations we assume that fiber-reinforced PPAM actuator can contract by 35% (slightly less than reported in the literature). For a relaxed length of 23mm, we obtain a contraction of 8mm per motor unit. For the example gait shown in Figure 8, a peristaltic cycle propels the robot forward by 24mm, and involves the contraction of 10 motor units.

The amount of H2O2 required for each motor unit actuation can be estimated assuming that the reaction product is an ideal gas:

where P is the operating pressure, Vg is the volume of gas produced, m is the mass of peroxide, Rh2o2 is the specific gas constant of reaction products of 70% peroxide, and Tadt is the adiabatic decomposition temperature of 70% peroxide (i.e., temperature of the gas after decomposition and before heat flows and work is done). Given that mass is conserved between the liquid and gas forms, one can express the mass in terms of the liquid density and volume, such that the ratio of volume of gas to liquid is:

where Vl is the volume of liquid peroxide, and  is the density of 70% peroxide. Based on an average operating pressure of 5 psig (about twice the pressure capability of the human diaphragm/lung), the resulting volume expansion ratio is approximately 1770. Since the conversion will entail energetic losses (e.g., heat flow), the volume conversion efficiency is assumed to be 67%, such that the actual volume expansion ratio (with losses) is approximately 1185. Based on the geometry of the contractile unit, the ratio of liquid volume to the differential volume of contraction (i.e., the volume of the contracted PPAM, less its relaxed volume) is approximately 6/1. As such, the contractile units will provide 7110 contractions, if all the peroxide is consumed. If we assume 90% of the peroxide is usable, we expect 6400 total contractions from each contractile unit. At 24mm per peristaltic cycle, or 2.4mm per contraction, the robot will have traveled 15.4 meters.

The speed of the robot is determined by the frequency of the peristaltic wave (i.e., is the product of the half period of the peristaltic wave and its frequency). Based on preliminary experiments, the inflation will occur (conservatively) in approximately 25 msec but the open-loop deflation time will be much longer; 225 msec. Thus the total time for contraction and expansion is approximately 250 msec, and the total time required for one peristaltic cycle is 1.5 seconds, corresponding to a velocity of 16 mm/sec, or 960 mm/min. The estimated speed and distance of travel are conservative and assume a peristaltic locomotion method that is well suited to cluttered environments but inefficient in open terrain. Even so, a robot with more modules can travel considerably further than 15 meters because not all the modules need to be actuated with every peristaltic cycle.

### Chembot concept 2: selectively morphing with asymmetric units

The second concept shares many features with the first, except that the storage units are not axisymmetric and the units are separated into storage and actuation units. The storage units are elastic and contain a significant volume of H2O2 in proportion to overall body size. They are asymmetric units, reinforced with flexible spines so that they bulge upward and outward. The extension units are a modified bellows construction, reinforced with fibers in the hoop direction so that they tend to expand axially, but not radially, when the fluid pressure in them is increased. Axial fibers may also be used so that when they are under internal hydrostatic pressure they do not buckle in compression.

When full of liquid H2O2, the storage units are relatively large. Consequently, for each storage unit to pass through a narrow aperture, most of the H2O2 must be forced out and into neighboring units. Evacuation of the fluid is accomplished by opening an internal valve that releases a small amount of H2O2 into an inner expansion chamber with a catalyst, as in the previously described concept. Additional valves at each end of the storage unit can be opened, to allow the flow of liquid H2O2 from one storage unit to another. In addition, by controlling the timing of the valves at each end of the elastic extension unit that connects two storage units, a controlled amount of axial extension can be achieved. In open terrain, where there is no need to evacuate and deflate a storage unit, all of the expansion in the storage units is converted to hydraulic actuation in the extension units.

The analysis of gas expansion for this concept is the same as for the first concept. However, it has the advantage that potentially more of the work of expansion of H2O2 is converted directly to forward travel with each contraction. With a greater forward speed and a significantly larger total volume of stored H2O2, it promises an order of magnitude greater distance of travel in open terrain.

Consequently this second concept will be evaluated in parallel with the first. If the manufacturing challenges associated with making sets of interconnected asymmetric hollow, reinforced inner and outer chambers can be overcome it will be continued; otherwise work will focus on the first concept to ensure having at least one approach that meets the Phase I demonstration objectives.

In summary, key features of both variants include:

A modular body with multiple, segmented interior chambers of highly elastic silicone and urethane materials, reinforced selectively with high strength tensile fibers. The initial body shape is an elongated worm or tentacle, but these bodies can be composed into different morphologies (e.g. branched like a sea star) for greatly diversified functional capabilities.

Catalyzation takes place directly in the actuation chambers for efficiency, simplicity and noise reduction.

The primary actuation cycle is open-loop, following a gait fixed by a microprocessor acting as a central pattern generator.

Regions of the outer skin are covered with directional adhesive materials (pioneered by Cutkosky’s group for Stickybot [Autumn06]) and the bodies are equipped with directional spines that bend easily in one direction but are stiffer when loaded in the opposite direction.

Low-power latching mechanisms can be used to join multiple sections together

## Materials and device fabrication

The robot structures will be fabricated by casting from elastomers capable of very high strains. The method of fabrication will be adapted from the Shape Deposition Manufacturing (SDM) process used to create Sprawl, Spinybot and Stickybot robots over the last several years [Cham02, Asbeck06, Kim07]. Carbon fiber fabric will be embedded where highest stiffness and strength are required. A silk mesh can be used where a flexible but inextensible membrane is desired for shear transfer (as in Stickybot toes, ). Discrete bands of Kevlar can be embedded for flexibility with high strength in a particular direction. Superelastic Nitinol wires can be embedded for a combination of moderate stiffness and large bending strains without plastic deformation.

SDM techniques for embedding fibers across material boundaries in heterogeneous structures are described in [Hatanaka03]. Using these methods, elastic strains of over 300% and a high fatigue life can be achieved if a smooth surface finish is maintained. The resulting structures have properties similar to tents or kites, in that the entire structure is capable of sustaining high loads and is surprisingly stiff, despite being made primarily of flexible and elastic materials. And like a tent, they can be collapsed as soon as the primary tension members are made slack.

Recently, the SDM process has been applied to complex, three dimensional hollow mesh structures of polymer, reinforced with a metal mesh and containing embedded fiber optic sensors [Park07] (Figure 12). A diagram of the manufacturing sequence is shown in Figure 13. This process can be adapted to create hollow fiber-reinforced chambers required for the current proposal.

Tendons, using steel or Vectran in Teflon sleeves, provide the possibility for remote actuation (Figure 11). Finally, in addition to the stiffening effects of fibers and tendons, narrow chambers can be filled with electro-rheological (ER) or magneto-rheological (MR) fluid for controllable resistance to deformation. These fluids have been used by Cutkosky [Akella95] to control soft robotic fingertips. In the energized state, the chambers become rigid up to the Bingham plastic flow stress; in the de-energized state they deform easily and provide damping. However, a drawback with ER fluids is the need for high voltages to achieve adequate field strength. For MR fluids, power must be supplied through electromagnetic coils or a mechanism must be devised to bring permanent magnets into proximity with the fluid on demand. Consequently, ER and MR fluids are not proposed as a primary enabling technology for this Phase I proposal.

SDM also supports the fabrication of directional dry adhesive patches, as demonstrated in Stickybot (Fig 9) [Kim07]. When a tangential force is applied to these patches in the preferred direction, they adhere to smooth surfaces and exhibit high friction on rough surfaces. This capability will allow the robot to climb slopes and to anchor itself for pushing its body into narrow cracks.

### Sensing and Control

The soft robot will use a largely open-loop control scheme, which will enhance actuation efficiency, reduce the number of required sensors, and reduce computational load on the microcontroller. A sequence of pulses commanded to the valves will generate one gait cycle. Variations in locomotion are enabled by varying the pulse widths and frequency, while entirely different modes of locomotion are enabled by varying the relative phasing of pulses. As in the Sprawl robots, a fixed motor pattern will determine the normal gait, and will be tuned in combination with the mechanical properties to achieve speed and dynamic stability [Cham02] (when creeping into cracks, stability is less of a concern because of the geometric constraint provided by the crack itself).

High level control involves behaviors using signals obtained from antennae and simple optical sensors to guide the robot across open spaces, detect small apertures, assess whether they can be entered, and monitor the progress of the robot into the aperture. The research tasks will include sensor interpretation for a combination of simple mechanoreceptors (antennae and force sensors on the limbs), pressure transducers, body deflection sensors, and simple optical sensors. This work will build upon prior results with the Sprawl robots [Cowan03] using antennae for guiding cockroach inspired robots along walls. We anticipate augmenting the antennae with other mechanical body sensors and with non-contact proximity sensors or specialized vision (e.g., simple optical flow or modified optical mouse technology). In prior work we have embedded such sensors into soft robotic fingertips [Howe93, Park07].

Control

The robot will leverage underactuation, with fewer controlled actuators than degrees of freedom, as a strategy to achieve functionality with minimum complexity. With proper constraints and dynamic tuning, underactuated systems can exhibit force/motion behaviors close to the biological “templates” from which they are derived, over a restricted range of conditions. A good example is the foot design in Stickybot that uses a single motor to actuate four toes that peel and curl around objects. The actuator is connected to the toes through a set of push-pull tendons connected via a double rocker-bogie linkage [Kim07].

### Operational challenges and steps taken to address them

Locomotion efficiency

Although several annelid robots have been reported in the literature [Jung07, Tsakiris05] the locomotion efficiency has generally been disappointing both in terms of body-lengths per locomotion cycle and in terms of meters per Joule. The previously developed devices have focused on reproducing authentic worm-like motion, rather than achieving very high values of deformation, which is of greater concern in the present case. The efficiency of locomotion is also directly related to the amount of deformation achieved per cycle. In open terrain, we anticipate gas expansion ratios of approximately 1200/1 at several psig. Consequently we anticipate approximately 0.75 meters of distance traveled per cm3 of peroxide consumed.  The annelid concept illustrated in Figure 8 is shown with 10 motor units, each of which carries a volume of 2cc of peroxide, such that the robot would provide a range of approximately 15 meters. Note that doubling the number of motor units would double the range (and corresponding duration of operation), and thus extend the range to 30 meters (i.e., 32 minutes of locomotion at 0.9 meters per minute). The second concept, shown in Figure 9, will potentially have a considerably greater locomotion efficiency at the expense of somewhat greater complexity.

Inside a narrow aperture or tube, locomotion efficiency and speed will be significantly reduced because maximum strains will also be reduced. However, with the addition of directional adhesive materials and directional spines (e.g. Figure 8 detail), we anticipate the ability to travel at 75% of the open-air speed.

Aperture penetration and traversal

The ability to traverse narrow spaces involves more than the ability to assume a narrow or flattened shape. It is also necessary to forcefully penetrate narrow openings, particularly if relying on the geometry of the opening to passively govern the deformed shape. For example, earthworms achieve substantial axial and radial forces – forces several times greater than the normal forces required for locomotion – in comparison to their body weight in order to penetrate soil [Quillin00]. Other animals such as arthropods use directional spines to help them push forcefully into tight spaces [Full97]. In the present case, we believe that it is necessary to use directional adhesive skin and directional spines to ensure that the body can anchor itself and push the distal end into an aperture. With directional skin, longitudinal forces of several times the body weight can be achieved [Kim07] and, because the materials are directional, detachment or disengagement is easily accomplished when the loading direction is reversed.

The directional skin and spines will also permit locomotion through extended apertures or tubes. The net amount of axial expansion and contraction will be much smaller than in open air, but little backward sliding will take place. Therefore (slow) forward locomotion will be possible. The price we pay for this capability is that backward motion through tubes will be difficult if not impossible. If the ability to move equally forward and backward through tubes is important, we will experiment with patches of opposite directionality on alternating segments which are selectively actuated, or not. The net locomotion efficiency will be reduced but bidirectional locomotion will be possible.

Electrical Power Requirements

The valves shown in the robot are slightly modified commercial valves (Lee 120 series), as shown in Figure 5, which are magnetically latching valves that require power only to switch.  Specifically, the valves require a 1 msec, 5 volt pulse across a 14 ohm coil or 70 mJ each time the valve is switched. Each valve is switched twice per cycle, and as such a ten-unit robot requires a total energy of 1.4 J per cycle.  As previously stated, since a cycle is expected to take 1.5 seconds, the average electrical power consumption for valve actuation is 0.93 W, which we approximate as 1 Watt. Note that this number will remain essentially invariant, regardless of the total number of contractile units in the robot.

The remaining power requirements for sensing and communication are modest and can easily be satisified by the same small lithium polymer battery that will be used for the valves.

Noise

Pneumatic equipment is often noisy as a consequence of releasing highly compressed gas at high flow rates, through small orifices. In the present case, we will be using low pressures and low flow rates. We will not be exhausting gas through small, rigid orifices. Consequently, we anticipate that the robot will operate more quietly than conventional small robots with RC servomotors and gearboxes. To further reduce noise we have the option to use elastomers such as urethanes, which have excellent sound dampening properties, for the outer skin.

# Phase I Proposed Plan of Work and Milestones

(Task numbers T1-T6 as listed in Table 1)

0-6 months:

Development

(T1) Design and build preliminary elastomeric body and appendage structures for testing – emphasis on valving, timing and motion generation.
(T1) Develop initial SDM manufacturing process for 3D fiber reinforced body structure.
(T2) Develop first version of valve control circuit and Li polymer battery with maximum width < 1cm
(T3) Begin development of communication system.
(T6) Research invertebrate models to find exemplars best matched to characteristics of robot. Develop test procedures for behaviors.

Tests:

(T2) Establish characteristics (speed, efficiency, leakage, peak temperature and pressure) of initial actuators.
(T5) Test radial and axial extension of structures as function of changes in internal pressure and correlate with predicted locomotion efficiency. Initial tests conducted using steam and/or compressed air while H2O2 valve/catalyst/actuator tests are conducted in parallel.
(T5) Ship first appendage structures from Stanford to Vanderbilt and Foster Miller and monopropellant actuation kits from Vanderbilt to Stanford.

6-month milestone: Tethered demonstration of peroxide-powered locomotion of soft robot segment (e.g. 3 DOF “tentacle”) able to: move forward using basic inflation/contraction cycle, steer gently to left or right, enter hole with tip contracted.

6-12 months:

Development:

(T1, T5) Develop 2nd generation Chembot with multiple segments and more DOF – able to bend left/right and up/down to locate apertures; able to crawl through aperture and recover shape on exit.
(T2) Develop improved valving and actuation system for 2nd generation Chembot prototype
(T3, T4) Develop flexible controller and battery for gait generation, sensor monitoring, communication.

Tests:

(T2, T5) Perform detailed experiments on 1st-generation structures to quantify locomotive speed, endurance, terrain capability, and payload capacity as function of H2O2 contained and consumed.
(T1) Characterize range of achievable shape change (percent change in body dimensions and correlation with maximum material strain).
(T1, T2) Characterize relationship among: dimensional change, pressure, volume of H2O2 dissociated and peak temperature reached.
(T5) Characterize traction forces between appendages and surfaces, and force available for insertion into apertures. Correlate with locomotion efficiency (meters traveled per cc of H2O2).
(T3, T4) Test communication with and steering of test structure using miniature camera.
(T3) Test electrical power consumption and correlate with mission requirements.
(T6) Conduct preliminary tests on selected animals to characterize locomotion efficiency and useful sensor-mediated behaviors that enhance ability to enter apertures.

12-month milestone: Tethered non-autonomous demonstration of peroxide-powered 2nd generation prototype with ability to locate and traverse aperture.

| Table 1: Division of Tasks, Effort and Metrics |
| --- |
| Tasks | Responsibility (% effort) | Metrics/milestones |
| T1: Body development | Primary: SU (40%) Secondary: FM, UV | 6mo: low DOF tentacle 12mo: multiple module tentacle 18mo: reconfigurable appendages |
| T2: Energy conversion, control | Primary: UV Secondary: SU, FM | 6mo: H2O2 actuation kit and preliminary performance measures 12mo: tests of H2O2 in body actuators for enhanced performance and efficiency 18mo: integrated body/actuator system with autonomous control |
| T3: Electronics, communication | Primary: shared between SU, FM, UV | 6mo: tethered communication and control 12mo: onboard visual package 18mo: flexible electronics packaging for untethered communication and control |
| T4: Sensing, behaviors | Primary: SU Secondary: VB, FM | 6mo: crawl through hole 12mo: locate and penetrate hole using onboard sensors + remote control 18mo: semi-autonomous navigation and reconfiguration |
| T5: Integration, testing | Primary: SU Secondary: FM | 6mo: characterize tentacle locomotion efficiency and correlate with body performance 12mo: off-axis aperture entrance and traversal 18mo: Phase I performance requirements and preliminary demonstration of body reconfiguration for different (e.g. branched) morphologies |
| T6: Bio-inspiration, tests | Primary: UCB | 6mo: identify optimal invertebrate locomotive model 12mo: identify bio-inspired approaches to sensor-mediated behavior for enhanced aperture detection & penetration 18mo: findings of targeted tests on animal strategies for detecting, penetrating aperatures and locomotion in confined spaces. |

12-18 months:

Development:

(T1-T4) 3rd generation autonomous prototype with ability to assemble prototypes to create different morophologies (e.g. branched, star shaped) with different functional capabilities.
3rd generation includes features of 2nd generation plus: improved flexible controller with provisions for assembly, external communication (input commands and output sensor data), onboard camera, integrated actuators.

Tests:

(T1, T2, T5) Continue mechanical tests as described above (6-12 month) on locomotion efficiency, speed and energy consumption, etc.
(T5) Conduct tests on ability to control direction and path, including for aperture entry and exit.
(T4, T6) Incorporate findings from bio-experiments to guide initial integration of sensory information into semi-autonomous behaviors for navigation and reconfiguration. 
(T4, T5) Develop behavioral specifications for fully autonomous operation (in Phase II)

18-month (Phase I) milestone/deliverable: Untethered demonstration of peroxide-powered soft robot, including demonstration of terrestrial locomotion, detection of an opening and traversal of an arbitrarily shaped aperture with a dimension of ~1cm.

Phase II (24 months): Work in Phase II will focus on refining the proof-of-concept from Phase I into a working robot with: (i) refinements in the design to increase performance, durability and reliability, (ii) a larger number of sensors and algorithms for interpreting sensor information and (iii) behaviors to increase autonomy with respect to typical task scenarios. An optional activity in Phase II will be to partner with a company to develop a pre-commercial prototype of the soft robot platform.

Relevant Prior Work

This proposal draws upon prior work in monopropellant-powered robotic and prosthetic devices and in bio-inspired soft robots. Prior work by Goldfarb [Goldfarb03, Fite06] has demonstrated that 70% H2O2 can be a compact, safe and controllable power source for prosthetic arms when coupled with pneumatic cylinders, a catalyst and a fluid control valve. For precise closed-loop control, pressure or force sensing is needed; in the present case we are using primarily open-loop control based on the empirically established time constant of each actuator unit.

In recent years, there has been much work in bio-inspired robots. In particular, the Sprawl family of hexapedal running robots developed by Cutkosky and Full [Cham02] and the climbing robots, Spinybot [Asbeck06] and Stickybot [Kim07] utilize the same Shape Deposition Manufacturing process that will be used in the current work.

A subset of the bio-inspired robotics literature specifically concerns soft robots inspired by annelids [Jung07, Tsakiris05], octopi [McMahan05], lampreys [Stefanini06], caterpillars [Trimmer06] and the amoeba [Hong05].

In most cases, the emphasis is on achieving a particular form of locomotion, rather than on achieving exceptional deformability as in the current proposal. However, the prior work provides numerous examples to draw upon for actuation and construction methods. In particular, several soft worm-like robots have been developed at. Paolo Dario's lab in Pisa, a leading European center for bio- robotics. Through collaboration with his laboratory, early experiments on vision-based guidance will be conducted on existing prototypes while the concepts described in this proposal are being fabricated.

Other related work includes numerous snake-like robots for pipe inspection and related tasks. Although they are not deformable in the same way as the robots in this proposal, they present related challenges for sensing, control and communications. Notable examples include the Pipe Mouse robot from S. Potter’s group at Foster Miller Inc.

# Facilities and Equipment

## UNIVERSITY OF CALIFORNIA, BERKELEY, Department of Integrative Biology, PolyPEDAL Lab

The PolyPEDAL Laboratory studies the locomotor biomechanics and energetics of small, many–legged animals. Our 1800 ft sq laboratory contains three types of workstations relevant to this proposal. The Motion-EMG-Kinematics workstations include 1 vertical treadmill with a see-through belt, 4 horizontal, minature treadmills, one rotating Styrofoam inertial treadmill, EMG amplifiers and high-speed video cameras for three-dimensional kinematic analyses. The Force-Kinetics workstations include three force sensitive platforms, and a photoelastic track for three-dimensional kinetics. The Metabolic Energetics Workstations allow measurement of oxygen consumption using O2 analyzers during steady-state locomotion. We also have access to the Biological Visualization Center with compound microscopes, a Cyberware laser scanner, and Compix/ImagePro image and morphometric analysis software. Other resources include walk-in cold rooms, centrifuges, computer rooms, a machine shop, an electrical shop, and a full time veterinarian. Campus facilities include an ecological scanning electronic microscope (Electroscan E3 ESEM) that allows pictures of living tissues, as well as conventional SEM (Hitachi S5000) and TEM (Tecnai 12).

Major Equipment:

3 Miniature force-platforms with 3 Vishay 8 channel amplifiers

photoelastic track

3 Power Mac computers with frame grabber and software for LabView, Analog-digital converters and Grass amplifiers for EMG

5 Mac and PC computers for simulation and data analysis

2 Portable incubators for controlling temperature

2 Kodak 1000 high-speed digital video cameras (1000 frames/sec)

4 Redlake high-speed digital video cameras (1000 frames/sec),

2 DALSA high-speed video cameras

2 NAC high-speed analog video cameras (color, 1000 frames/sec)

3-D Motion Analysis System (Motus, Peak Performance Tech. Inc.) Dedicated PC computer for studies on mechanics and video analysis

2 Perturbation / muscle lever systems

4 miniature treadmills, 1 Styrofoam rotating inertial ball, 1 Vertical treadmill

3 oxygen analyzers

Dissecting microscopes (Nikon)

## STANFORD UNIVERSITY, Department of Mechanical Engineering:  Center for Design Research and Rapid Prototyping Lab

Facilities at Stanford University for fabrication of flexible multi-material prototypes are located in the Center for Design Research(CDR) and Rapid Prototyping Lab (RPL) in the Department of Mechanical Engineering. Where appropriate, the Stanford Nanofabrication Facility is available for sensor development.

The Biomimetics and Dexterous Manipulation lab in MERL Bldg. 660 Room 132 includes industrial robots, bio-inspired robot legs and hands and specialized equipment for the design and fabrication of bio-inspired robots and sensors. Various measurement systems allow motions (via high-speed video tracking), ground reaction forces, accelerations, and contact stresses to be measured for robotic appendages with embedded electronic and optical sensors. Additionally, the Stanford Center for Design Research comprises approximately 4000 sq. feet of space with workstations for computer-aided design and rapid 
prototyping and systems for video-conferencing with collaborators.

The Rapid Prototyping Laboratory (RPL) is a 3554 sq ft facility equipped with a variety of manufacturing equipment to support the entire process sequence for metal, polymer and ceramic parts created using the Shape Deposition Manufacturing (SDM) technique. A dedicated UV-light station serves to create base building blocks of water-soluble UV-curable sacrificial material (solder mask). The milling of the sacrificial support material is performed at two CNC stations: Haas VF-0E 3-axis CNC mill and MAHO MH 600-C 5-axis CNC mill. Wax casting, removal of solder mask in forced-flow water tanks, and vacuum casting of uncured polymer or ceramic slurry into the wax molds is also supported by dedicated stations at RPL. The "green" un-sintered parts are dried in controlled humidity environment of anenvironmental chamber (Thermotron SM-3.5S). Finally the dried "green" parts are sintered in high temperature furnace (Thermal Technology Inc). Additional facilities are available for spin-coating, sputtering, and UV lithography. A new addition to the facility includes a clean room section with a confocal microscope and atomic layer deposition station.

The Stanford Nanofabrication Facility is used to fabricate parts that require machines with further precision than the equipment found in RPL and MERL. It is located in the Center for Integrated Systems and includes a 10,500 square foot Class 100 cleanroom that is populated with nearly 100 different instruments and fabrication tools. SNF supports a broad range of micro- and nanofabrication materials and processes. In addition the capabilities of the SNF, users can make use of the advanced characterization tools (e.g. SEM, TEM and FIB) offered by the Stanford Nanocharacterization Laboratory (SNL) located adjacent to the SNF.

## Vanderbilt University

## Foster Miller

# Management Plan

Stanford University (Cutkosky) will be the project lead, as main platform fabricator and integrator. The management will draw upon his experience as P.I. for an ONR MURI on the Sprawl robots and as a major partner in the DARPA RiSE Biodynotics consortium responsible for designing and fabricating the Sprawl, Spinybot and Stickybot robot platforms. Goldfarb (Vanderbilt), Full (Berkeley) and Potter (Foster Miller Inc.) also have extensive experience with multi-institutional DARPA programs.

Potter’s experience with Pipe Mouse has already been invaluable in the weekly teleconferences leading to the production of this proposal. In Phase II, Foster Miller Inc. can provide a path toward pre-commercial prototypes for testing in applications scenarios.

The project also takes advantage of Cutkosky’s interactions with the laboratory of Prof. Paolo Dario in Pisa, Italy. Dario’s laboratory is a leading European center in bio-robotics and has constructed worm, lamprey and polychaete inspired robots that are widely cited in the literature. Although these robots are only moderately deformable, they can be used for testing sensing and guidance strategies while developing, concurrently, the primary actuation and body mechanisms for our soft Chembot.

As in the previous Sprawl and ongoing DARPA RiSE projects we will have frequent exchanges of personnel and hardware, in addition to a weekly videoconference meeting. In particular:

A Vanderbilt researcher will spend a significant period during first quarter at Stanford, learning how to do SDM fabrication. (Dario’s lab has already learned how to do Shape Deposition Manufacturing as a result of Cutkosky’s 6-month visit there in 2002.)

A Stanford researcher will spend time at VU learning how to handle and control peroxide monopropellant.

A Stanford researcher will spend 1 day per week in the laboratory of Full at Berkeley, participating in focused animal experiments (e.g., use of sensory information, behaviors for reliable entry).

A researcher from Dario’s lab will spend 6 months at Stanford working with Cutkosky’s group and collaborating with Potter on robot steering and sensing methods.

In addition, at approximately 6 months, initial appendage structures will be shipped from Stanford to Vanderbilt and a “kit” of miniature monopropellant valves, catalyst and controller will be shipped from Vanderbilt to Stanford so that both sites have equivalent first-generation hardware. The materials costs for the soft robot are not high; therefore subsequent generations of the soft robot will also be distributed between Vanderbilt and Stanford.

## Personnel

Mark R. Cutkosky is a professor in the Dept. of Mechanical Engineering at Stanford University. He joined Stanford in 1985, after working in the Robotics Institute at Carnegie Mellon University and as a machine design engineer at ALCOA. Cutkosky's research includes robotic manipulation and tactile sensing and the design and fabrication of biologically inspired robots. He has graduated 30 Ph.D. students and published extensively in these areas, including several patents. He consults with various companies and serves on technical advisory boards in the areas of robotics and human/computer interaction devices. His research focuses on novel multi-material fabrication methods to create robots whose mechanical properties draw inspiration from insects, geckos and other animals to increase physical robustness, improve performance and simplify control. His work, partly in collaboration with biologist Robert Full, has been featured in Forbes, Discover Magazine, The New York Times and other publications and has appeared on the CBS Evening News, Next @CNN, Science Central News and other popular media. His most recent work on Spinybot and Stickybot has won a Best Video award (IEEE ICRA06), Best Student Paper award (IEEE ICRA07), Finalist, Best Manipulation Paper (IEEE ICRA07) and TIME Magazine Best Inventions of 2006. Cutkosky’s previous awards include several Best Paper awards, a Fulbright Distinguished Faculty Chair (2002), a Charles M. Pigott Professorship (1996) at Stanford University and an NSF Presidential Young Investigator award (1986).

Robert J. Full joined the University of California at Berkeley as an Assistant Professor of Zoology in 1986. In 1997 Full became a Chancellor’s Professor at Berkeley, awarded for “distinguished achievement of the highest level in research, teaching and service.” Full has authored over 200 contributions and has delivered an equal number of national and international presentations. In 2006 he founded, CIBER, a new center at Berkeley dedicated to Interdisciplinary Biological-inspiration in Education and Research. In 1990 he received a Presidential Young Investigator Award. He has mentored over 90 undergraduate researchers who have received more than 50 awards/fellowships. For these efforts he recently was named Mentor in the Life Sciences by the National Academy of Sciences. Full directs the Poly-PEDAL Laboratory, which studies the Performance, Energetics and Dynamics of Animal Locomotion (PEDAL) in many-footed creatures (Poly). His research program in comparative physiology and biomechanics has shown how examining a diversity of animals leads to the discovery of general principles of locomotion. His fundamental discoveries have inspired the design of novel neural control circuits, artificial muscles, eight autonomous legged robots and the first self-cleaning dry adhesive.

Michael Goldfarb: Michael Goldfarb is a Professor in the Department of Mechanical Engineering at Vanderbilt University, and director of the Center for Intelligent Mechatronics.  Dr. Goldfarb joined the faculty at Vanderbilt immediately after receiving his Ph.D. from the Department of Mechanical Engineering at MIT in 1994.  Dr. Goldfarb has published over 100 technical papers in the areas of robot design and control, including relevant work in the areas of liquid hydrogen peroxide powered robotics and the design of minimally-actuated elastodynamic robotic insects. He has directed over $10 million of externally funded research over the past dozen years as a principal investigator from federal agencies including the NSF, NIH, DARPA, NASA, the CIA and ARO. Dr. Goldfarb has been funded through seven different DARPA programs over the past ten years, as lead on five of those seven. Two of those programs were for mesoscale robotics, and three were/are relevant to hydrogen peroxide based power for robot actuation.

Steve Potter/Foster Miller blah blah blah

# Current and Pending Support

Mark Cutkosky

Current

Title: Smart robot appendages with integrated actuators, sensors and preflexes – postdoctoral fellowship

Source: National Imagery & Mapping Agency, NGA501-05-BAA-0003

Location: Stanford University, MERL 132

Period: 07/25/05 - 07/30/07

Total award amount:  $240,000

PI Person-months/year:  ¼  (advisor to post-doctoral fellow)

Title: Robots in Scansorial Environments – DARPA Biodynotics

Source: DARPA/University of Pennsylvania

Period: 04/11/05 - 08/31/08

Location: Stanford University, MERL 132

Total amount: $1,385,423

PI Person-months/year:  2

Title: Z-man

Source: DARPA/Draper Labs

Period: 04/09/07 - 08/31/07

Location: Stanford University, MERL 132

Total amount: $186,000

PI Person-months/year:  2

Title: Embedded Fiber Optic Sensors for Human-Safe Robot Limbs

Source: NASA/IFOS

Period: 02/01/05 – 07/01/05

Location: Stanford University, MERL 132

Total amount:  $100,000

PI Person-months/year:  ½

Pending

Title: Active Nanostructures and Nanosystems

Source: UCSB/NSF NIRT

Period: 05/01/07 - 04/30/11

Location: Stanford University, MERL 132

Total amount:  $425,000

PI Person-months/year:  ½

Michael Goldfarb

Robert Full

Current

Title:  NIRT: Biologically Inspired Synthetic Gecko Adhesives

Source: NSF Award # 0304730

Location: U.C. Berkeley

Period: 9/1/2003 – 8/31/2007

Total award amount:  $290,989

PI Person-months/year:  ½

Title: RiSE: Robotics in Scansorial Environments

Source: DARPA/University of Pennsylvania

Period: 08/1/2003 – 08/31/2008

Location: U.C. Berkeley

Total award amount:  $1,047,561

PI Person-months/year:  1

Title:  FIBR:  Neuromechanical Systems Biology

Source: NSF Award # 0425878

Period: 9/1/2004 – 8/31/2009

Location: U.C. Berkeley

Total award amount:  $2,970,853

PI Person-months/year:  1

Title:  Modeling Robot-Ground Interactions

Source:  DOD National Geospatial Intelligence Agency  HM1582-06-1-2019

Period: 9/6/2006 – 9/5/2007

Location: U.C. Berkeley

Total Award Amount: $120,000

PI Person-months/year:  1 (advisor to post-doctoral fellow)

Steve Potter

# References

[Akella95] P. Akella and M.R. Cutkosky, “Contact Transition Control with Semi-active Soft Fingertips,” IEEE Transactions on Robotics and Automation, v. 11, n 6, 1995, pp. 859-865.

[Asbeck06] A. Asbeck, S. Kim, M.R. Cutkosky, W.R. Provancher and M. Lanzetta, “Scaling Hard Vertical Surfaces with Compliant Microspine Arrays,” IJRR, v 15, n. 12, 2006, pp. 1165-1180.

[Autumn06] K. Autumn, A. Dittmore, D. Santos, M. Spenko and M. Cutkosky, "Frictional adhesion: a new angle on gecko attachment," Journal of Experimental Biology, 209, 3569-3579 (2006)

[Barnes93] R.B. Barnes. Introduction to the Onychophora, Chilopoda, and lesser Protostomata, pp. 1-9 in Harrison FW, Rice ME (eds.).  Microscopic anatomy of invertebrates, vol. 12 Onychophora, Chilopoda, and lesser Protostomata. Wiley-Liss, NY, 1993.

[Cham02] J.G. Cham, S.E. Bailey, J.C. Clark, R.J. Full and M.R. Cutkosky, "Fast and Robust: Hexapedal Robots via Shape Deposition Manufacturing," IJRR, v 21, n 10-11, 2002, p 869-882.

[Cowan03] N. Cowan, E.J. Ma, and M.R. Cutkosky and R.J. Full, “A Biologically Inspired Passive Antenna for Steering Control of a Running Robot,” Proc. ISRR, Siena, Italy, Oct. 2003.

[Cuevas07] http://www.fs.fed.us/r8/caribbean/wildlife-facts/2002/wildlife-facts-april-2002.shtml

[Daerden02] F. Daerden, D. Lefeber, “Pneumatic Artificial Muscles: Actuators for Robotics and Automation,” European Journal of Mechanical and Environmental Engineering, 2002, 47(1), pp. 10-21.

[Fite06] K.B. Fite, J. Mitchell, E.J. Barth, and M. Goldfarb, “A Unified Force Controller for a Proportional-Injector Direct-Injection Monopropellant-Powered Actuator,” ASME Journal of Dynamic Systems, Measurement and Control, v 128, n 1, pp. 159-164, 2006.

[Fite06b] K.B. Fite, and M. Goldfarb, “Design and Energetic Characterization of a Proportional-Injector Monopropellant-Powered Actuator,” IEEE/ASME Trans on Mechatronics, v 11, n 2, pp. 196-204, 2006.

[Full97] R.J. Full, Invertebrate locomotor systems. 1997. In: The Handbook of Comparative Physiology. (ed. W. Dantzler). Oxford University Press. pp. 853-930.

[Goldfarb03] M. Goldfarb, E.J. Barth, M.A. Gogola, and J.A. Wehrmeyer, “Design and Energetic Characterization of a Liquid-Propellant-Powered Actuator for Self-Powered Robots.” IEEE/ASME Trans on Mechatronics, v 8, n 2, pp. 254-262, 2003.

[Hatanaka03] M. Hatanaka and M.R. Cutkosky, “Process Planning for Embedding Flexible Materials in Multi-material Prototypes" DETC ASME, 2003, Chicago, Illinois, USA, Sept. 2003.

[Howe93] R. Howe and M. R. Cutkosky, “Dynamic Tactile Sensing: Perception of Fine Surface Features with Stress Rate Sensing,” IEEE Trans on Robotics and Automation, v 9, n 2, April, 1993, pp. 140-151.

[Hong05] D.W. Hong, “A Biologically Inspired Whole Skin Locomotion Strategy for Mobile Robots,” US-Korea Conference on Science, Technology and Entrepreneurship (UKC2005), 2005, pp. 11-13.

[Jung07] K. Jung, J.C. Koo, J-D Nam, Y. K. Lee and H. R. Choi “Artificial Annelid Robot Driven by Soft Actuators,” Bioinspiration & Biomimetics, v 2, pp. S42-S49, 2007.

[Kim07] S. Kim, M. Spenko, S. Trujillo, B. Heyneman, V. Mattoli, M.R. Cutkosky, "Whole body adhesion: hierarchical, directional and distributed control of adhesive forces for a climbing robot," IEEE ICRA07, April 2007.

[McMahan05] W. McMahan, B.A. Jones, I.D. Walker, “Design and implementation of a multi-section continuum robot: Air-Octor,” IEEE IROS05, 2005, pp. 2578-2585.

[Park07] Y-L Park, K. Chau, R.J. Black, and M.R. Cutkosky, "Force Sensing Smart Robot Fingers using Embedded Fiber Bragg Grating Sensors and Shape Deposition Manufacturing," IEEE ICRA07, April 2007.

[Quillin00] K. J. Quillin, “Ontogenetic Scaling of Burrowing Forces in the Earthworm Lumbricus Terrestris,” Journal of Experimental Biology, v 203 pp. 2757-2770.

[Saranli01] U Saranli, M Buehler, D.E. Koditschek, “RHex: A Simple and Highly Mobile Hexapod Robot,” IJRR, v 20, n. 7, 2001, pp 616.

[Shields06] B.L. Shields, K. Fite, and M. Goldfarb, “Design, Control, and Energetic Characterization of a Solenoid Injected Monopropellant Powered Actuator,” IEEE/ASME Trans on Mechatronics, v 11, n 4, pp. 477-487, 2006.

[Shinichi01] H. Shinichi, M. Tomohiro, and K. Sadao, Prototyping Pneumatic Group Actuators Composed of Multiple Single-motion Elastic Tubes, IEEE ICRA01, April 2001.

[Stefanini06] C. Stefanini, G. Orlandi, A. Menciassi, Y. Ravier, G. La Spina, G. S. Grillner, P. Dario, “A Mechanism for Biomimetic Actuation in Lamprey-like Robots,” The Firrst IEEE/RAS_EMBS International Conference on Biomedical Robotics and Biomechatronics, 2006, pp. 579—584.

[Trimmer06] B.A. Trimmer, A.E. Takesian, B.M. Sweet, C.B. Rogers, D.C. Hake, D.J. Rogers. (2006). Caterpillar locomotion: A new model for soft-bodied climbing and burrowing robots. In 7th International Symposium on Technology and the Mine Problem. Monterey, CA: Mine Warfare Association.

[Tsakiris05] D.P. Tsakiris, M. Sfakiotakis, A. Menciassi, G. la Spina, and P. Dario, “Polychaete-like Undulatory Robotic Locomotion,”   IEEE ICRA05, April 2005.

# Comments

I took out “precise control,” since I don’t want readers to misconstrue our control intentions in this work.

# Text boxes

Figure 4. Peripatus (top) and Guilding’s Sea Star (bottom) are two examples of selectively compliant animals that penetrate small areas in proportion to normal body size.

Figure 2. Compliant Chembot tentacle approaching and traversing a narrow aperture

Figure 11. Example multi-material, under-actuated system fabricated by SDM: Four toes are controlled using a single actuator through a double-differential linkage and push-pull tendons. The toes are fabricated from 4 different grades of polymer, with fabric inserts [Kim07].

Figure 12. Example of hollow polymeric structure with embedded fibers made using Shape Deposition Manufacturing [Park07].

Figure 8. Annelid concept with alternating angled units to permit steering. Shown mid-way through peristaltic wave cycle.

Figure 13. SDM process for creating hollow polymer mesh finger with embedded fibers.

Figure 6. Concept of deformable monopropellant and actuator system.

Figure 5.Examples of (conventional scale) Kevlar-reinforced artificial muscle “PPAM” actuators and micro-dispensing valve (Lee VHS-EPSVseries 120).

Figure 3. Example multiple segments assembled to create a new morphology with new capabilities.

Figure 9. Asymmetric Chembot with separate storage and actuation units

Figure 14. SDM fabrication process and scanning electron microscope image of directional dry adhesive used on Stickybot for climbing smooth vertical surfaces

Figure 1. (a) Chembot basic unit can be thrown through a window (b) After uncoiling and expanding, it can selectively deflate segments to progress through a small aperture.

| Table I: Chembot Metrics | In open areas | In 1cm x 1cm aperture |
| --- | --- | --- |
| Locomotion type | Initial: peristaltic wave Ultimate: crawling with wave gait | Peristaltic wave, assisted by directional skin and spines |
| Velocity (meters per minute) | Initial: 0.9 meters/min Ultimate: ?? | 0.9 meters/min |
| Range (meters) | Initial: 1.5 meters/motor unit (15 meters for a 10-unit design, 30 meters for a 20-unit design) Ultimate: ?? | 1.5 meters/motor unit |
| Energy (J/m) | Initial: ?? Ultimate: ?? | To be filled in |
| Electrical power requirements (W) | Initial: 100 mW/motor unit (i.e., 1 W for a 10 motor-unit design, 2 W for a 20 motor-unit design) Ultimate: ?? | To be filled in |
| Maximum hole depth that can be traversed (cm) | No upper limit, other than range of robot |
| Type of power generation system | Catalyzed expansion of 70% H2O2 in elastic actuation chambers |
| Morphing mechanisms | Initial: Active expansion + passive contraction acting on liquid and inflatable chambers; Ultimate: add ability to join modular units to change configuration. |
| Primary component hardness (e.g. phase change, composition of elements) | Initial: Liquid/gas phase transition acting against elastomers with selective fiber reinforcement; Ultimate: attachment of modular tentacle units. |

Figure 7. Detail of module activation

Figure 10. Schematic of storage unit and valves